## Slide 1
Meddle: Middleboxes for Increased Transparency and Control of Mobile Traffic
Ashwin Rao, David Choffnes, Justine Sherry, Arnaud Legout, Arvind Krishnamurthy, Walid Dabbous
Goals
Transparency
  Provide comprehensive view of mobile traffic regardless of device, OS, access technology, & ISP
  Characterize network behavior of apps
  Identify ISP policies
Control
  Manipulate mobile traffic to enact arbitrary policies
  Facilitate user-specific policy management
Coverage
  Incentives for large scale adoption
  Scale to support a large number of users
  Supports user mobility
  Easy to deploy (does not need OS modifications or ISP support)
VPN Server
Meddlebox
Meddle Server
Policy
Datastore
Internet
DNS
Packet
Filter
Traffic
Monitors
Web Proxy
Open vSwitch
Meddlebox
Motivation
Opaque mobile ecosystem
  Limited knowledge on the network usage of apps
  No visibility into what ISPs are doing to traffic
Limited control
  Locked down operating systems
  ISPs solely control network policies
VPN Server
Meddlebox
Meddle Server
System Architecture
Viability
Current implementation
  Supports iPhone and Android, uses open source VPN server
Power consumption
  Increases by about 10%
  E.g., 24-hour charge now lasts 22 hours.
Data consumption
  Increases by 8—12%
  Offset this through ad blocking and compression
Network latency
  Expected to increase by 3 ms to 13 ms
  Insignificant portion of 3G latencies
Research Enabled by Meddle
Privacy and Security
    Detect privacy invasive traffic
    Malware detection and blocking
Characterization
  Automatically detect ISP policies
  Impact of network behavior of OS and apps
Exploring network optimizations
    HTTP (Split-browser, SPDY push, etc.)
    Proxying and caching
New protocols and communication models
    Peer to Peer offloading
    Transparent support for emerging technologies such as DNSSEC and IPv6
  Routing, scalability, and management
    Automatically and correctly compose multiple Meddleboxes
    Performance and reliability in a cloud environment
ashwin.rao @ inria.fr ; choffnes @ cs.uw.edu ; justine @ eecs.berkeley.edu ; arnaud.legout @ inria.fr ; arvind @ cs.uw.edu ; walid.dabbous @ inria.fr
Example Applications
Device wide ad blocking
Transparent web proxy
Traffic compression
Visualize interaction between apps and trackers